## Slide 1
Simulator
getTime(); getTimeLimit()
getRealTime()
getEventQueue()
getWorkManager()
RunSimulation():
while self.getTime() < self.getTimeLimit():
# weekendjump
if self.getTime() % self.shift_minutes == 0:
applyShiftChange()
executeEvents()
executeEvents():
# handle pending events: getWorkManager().HandleSimEvent(e)
for e in self.getEventQueue()["Preemptables"]:
if not e.IsActive():
getWorkManager().resumeSimEvent(e)
ShopFloor Manager
DataManager
getProductionOrders()
createInstance():
DataManager. ReadResources()
DataManager. ReadDemandFile()
applyShiftChange():
# preempted events are suspended.
# execution block is closed.
# resource availabilities are set.
HandleSimEvent(e):
if e.getEquipment() == None or e.getResource() == None:
# execute decisions for the event e.
if e.getEquipment() != None and e.getResource() != None:
ProceedToScheduling(e)
resumeSimEvent(e):
if e.getEquipment() == None or e.getResource() == None:
# execute decisions for the event e.
if e.getEquipment() != None and e.getResource() != None:
ProceedToScheduling(e)
ProceedToScheduling(e) :
OprMove => e
OprMove => BringEquip => e
BringEquip => e

## Slide 2
Creating pending events
Buffer():
self.getPendingEvent() # outputbuffer: TL, #inputbuffer: MS
addItem(): # very first happen at central buffer
generateEvent()
generateEvent():
if len(self.getItems()) > 0 and self.getPendingEvent() == None:
if not self.isInputType(): #output buffer
load_event_type = self.getWorkMgr().getEventTypes()["Trailer Loading"]
else: # input buffer
setup_event_type = self.getWorkMgr().getEventTypes()["Machine Setup"]
self.getSimulator().ScheduleEvent(self.getPendingEvent())
Simulator
getTime(); getTimeLimit()
getRealTime()
getEventQueue()
getWorkManager()
RunSimulation():
while self.getTime() < self.getTimeLimit():
# weekendjump
if self.getTime() % self.shift_minutes == 0:
applyShiftChange()
executeEvents()
executeEvents():
# handle pending events: getWorkManager().HandleSimEvent(e)
for e in self.getEventQueue()["Preemptables"]:
if not e.IsActive():
getWorkManager().resumeSimEvent(e)
ScheduleEvent(e):
if e.getEquipment() == None or e.getResource() == None:
if not e in self.getEventQueue()["Pending"]:
self.getEventQueue()["Pending"].append(e)
else:
self.getEventQueue()[self.getTime()].append(e) # event can start
ShopFloor Manager
HandleSimEvent(e):
if e.getEquipment() == None or e.getResource() == None:
# execute decisions for the event e.
if e.getEquipment() != None and e.getResource() != None:
ProceedToScheduling(e)
resumeSimEvent(e):
if e.getEquipment() == None or e.getResource() == None:
# execute decisions for the event e.
if e.getEquipment() != None and e.getResource() != None:
ProceedToScheduling(e)
startSimEvent(e):
if e.getResource().isAvailable() and e.getEquipment().isAvailable(): #
execute decisions for the event e.
e.setActive()
if e.getEventType().isPreemptable():
if e.getEventType().isProcess():
e.getProgressDict()[event.getEquipment()].append((self.getSimulator().getTime(),0))

## Slide 3
Create event
Eq and Res assigned?
Yes
Put into
Simulator.pending
Check create preparation events
No
Handle event
Simulator time tick
PE
TT
TU
MS
Pr
MU
ML
Check create preparation events
TL

## Slide 4
Event | Eq. | Resource | Pending | Loc/Place | Con. Pred | Def. Pred. | Direct Fol. | Preempt | Item Sel
TL | Tr | Opr | + | M Out | OM,BE | - | - | - | +
TT | Tr | Opr | - | M>M Out>Inp. | - | TL | + | - | -
TU | Tr | Opr | - | M Inp. | - | TT | + | - | +
MS | M | Opr | + | M M | OM | - | - | - | +
ML | M | Opr | + | M Inp | OM | MS | + | + | -
Process | M | M | - | M | - | ML | + | + | -
MU | M | Opr (Man) | + | M Out | OM | Process | + | + | -
OM |  |  |  |  |  |  |  |  | 
BE |  |  |  |  |  |  |  |  | 

## Slide 5
Event | Stage | Type
TL | Handle | Assign Equipment
TL | Handle | Assign Resourse
TL | Handle | Select Items
TT | Handle | Select Destination
TU | Start | Select Items
MS | Handle | Assign Resource
MS | Handle | Select Items
ML | Resume | Assign Resource
MU | Resume | Assign Resource
Processing | Resume | AssignEquipment*